## Slide 1: EEL 4781 Computer Communication Networks Chapter 1-3: Introduction to Networking Concepts
Xin Xin
Department of Electrical and Computer Engineering
University of Central Florida

## Slide 2: Agenda
Protocols and Protocol Layers
  protocol
  layers
  encapsulation
Security
History
Summary

## Slide 3: Protocols and Protocol Layers
What’s a protocol?
A human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Notes: Explain important points
distributed entities, exchanging messages (governed by protocols)
Time going down
go over definition of protocol (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 4: Protocols and Protocol Layers
What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
… specific messages sent
… specific actions taken when message received, or other events
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 5: Protocols and Protocol Layers
Protocol “layers” and reference models
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 6: Protocols and Protocol Layers
Example: organization of air travel
airline travel: a series of steps, involving many services
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 7: Protocols and Protocol Layers
Example: organization of air travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
ticketing service
baggage service
gate service
runway service
routing service
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
Q: describe in words the service provided in each layer above

## Slide 8: Protocols and Protocol Layers
Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change in layer's service implementation: transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?
layering in other complex systems?

## Slide 9: Protocols and Protocol Layers
Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 10: Protocols and Protocol Layers
Internet protocol stack
application: supporting network applications
  IMAP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 11: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!

## Slide 12: Network security
Bad guys: malware
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam or distributed denial of service (DDoS) attacks

## Slide 13: Network security
Bad guys: packet interception
packet “sniffing”:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
Bad guys: fake identity
IP spoofing: send packet with false source address
spoofing
sniffing

## Slide 14: Network security
Bad guys: denial of service
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts

## Slide 15: Network security
Lines of defense:
authentication: proving you are who you say you are
  cellular networks provides hardware identity via SIM card; no such hardware assist in traditional Internet
confidentiality: via encryption
integrity checks: digital signatures prevent/detect tampering
access restrictions: password-protected VPNs
firewalls: specialized “middleboxes” in access and core networks:
    off-by-default: filter incoming packets to restrict senders, receivers, applications
    detecting/reacting to DOS attacks

## Slide 16: History
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles
Larry Robert

## Slide 17: History
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
1972-1980: Internetworking, new and proprietary nets
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best-effort service model
  stateless routing
  decentralized control
define today’s Internet architecture

## Slide 18: History
1983: deployment of TCP/IP
1982 - 1988: smtp e-mail protocol defined； DNS defined for name-to-IP-address translation； ftp protocol defined； TCP congestion control
new national networks: CSnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks
Robert Kahn
Vinton Cerf

## Slide 19: History
early 1990s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web (World Wide Web application)
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990s: commercialization of the Web
late 1990s – 2000s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000s: commercialization, the Web, new applications
Tim Berners Lee

## Slide 20: History
  aggressive deployment of broadband home access (10-100’s Mbps)
2008: software-defined networking (SDN)
increasing ubiquity of high-speed wireless access: 4G/5G, WiFi
content/service providers (Google, FB, Microsoft) create their own networks
    bypass commercial Internet to connect “close” to end user, providing “instantaneous” access to social media, search, video content, …
enterprises run their services in “cloud” (e.g., Amazon Web Services, Microsoft Azure)
rise of smartphones: more mobile than fixed devices on Internet
rise of IoTs: ~15B devices attached to Internet
2005-present: more new applications, Internet is “everywhere”

## Slide 21: Chapter 1: summary
We’ve covered a “ton” of material!
Internet overview
network edge, access network, core
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
protocol
layering, service models
security
history
You now have:
context, overview, vocabulary, “feel” of networking
more depth, detail, and fun to follow!

## Slide 22
Thanks
Acknowledgment
The materials for this course are in part based upon the materials from a number of people/sources, including:
Official website of the Kurose and Ross text: Computer Networking: A Top-Down Approach
Official website of the Tanenbaum & Wetherall text: Computer Networks
Dr. Murat Yuksel: https://www.ece.ucf.edu/~yuksem/teaching/EEL-4781-Fall-2020.html
Dr. Raj Jain: https://www.cse.wustl.edu/~jain/