## Slide 1: EEL 4781 Computer Communication Networks Chapter 2-2: Application Layer
Xin Xin
Department of Electrical and Computer Engineering
University of Central Florida

## Slide 2: Agenda
Web
  HTTP Protocol
  HTTP Improvement
  Web Caches
Email
  SMTP Protocol
FTP (Optional) discussion only*

## Slide 3: HTTP (continued)
Non-persistent HTTP: response time
RTT (Round Trip Time): time for a small packet to travel from client to server and back
HTTP response time (per object):
one RTT to initiate TCP connection
Why? Allocating resources?
one RTT for HTTP request and first few bytes of HTTP response to return
object/file transmission time
time to
transmit
file
initiate TCP
connection
RTT
request file
RTT
file received
time
time
Non-persistent HTTP response time = 2RTT+ file transmission time

## Slide 4: HTTP - Protocol
HTTP overview (continued)
Identifier
  IP and port number: 80
  URL (Uniform Resource Locator)
Protocol
  Format
  Types
Services
  Sockets
Challenges
  Non-persistent (HTTP/1.0)
  Stateless
HTTP/1.0
HTTP/1.1
HTTP/2
Cookies

## Slide 5: HTTP - Protocol
HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
header
lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Mozilla/5.0 (Macintosh; Intel Mac OS X 10.15; rv:80.0) Gecko/20100101 Firefox/80.0 \r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Connection: keep-alive\r\n
\r\n
carriage return character
line-feed character
request line (GET, POST,
HEAD commands)
carriage return, line feed at start of line indicates end of header lines

## Slide 6: HTTP - Protocol
HTTP request message: general format
request
line
header
lines
body
method
sp
sp
cr
lf
version
URL
cr
lf
value
header field name
cr
lf
value
header field name
~
~
~
~
cr
lf
entity body
~
~
~
~

## Slide 7: HTTP - Protocol
Other HTTP request messages
POST method:
Submit data to the server, usually to create or update a resource
user input sent from client to server in entity body of HTTP POST request message
GET method :
Retrieve data from the server
HEAD method:
requests headers (only) that would be returned if specified URL were requested with an HTTP GET method.
PUT method:
uploads new file (object) to server
completely replaces file that exists at specified URL with content in entity body of POST HTTP request message

## Slide 8: HTTP - Protocol
HTTP response message
status line (protocol
status code status phrase)
header
lines
data, e.g., requested
HTML file
HTTP/1.1 200 OK
Date: Tue, 08 Sep 2020 00:53:20 GMT
Server: Apache/2.4.6 (CentOS) OpenSSL/1.0.2k-fips PHP/7.4.9 mod_perl/2.0.11 Perl/v5.16.3
Last-Modified: Tue, 01 Mar 2016 18:57:50 GMT
ETag: "a5b-52d015789ee9e"
Accept-Ranges: bytes
Content-Length: 2651
Content-Type: text/html; charset=UTF-8
\r\n
data data data data data ...

## Slide 9: HTTP - Protocol
HTTP response status codes
200 OK
  request succeeded, requested object later in this message
301 Moved Permanently
  requested object moved, new location specified later in this message (in Location: field)
400 Bad Request
  request msg not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
status code appears in 1st line in server-to-client response message.
some sample codes:

## Slide 10: HTTP - Improvement
Persistent HTTP (HTTP/1.1)
Non-persistent HTTP issues:
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open multiple parallel TCP connections to fetch referenced objects in parallel
Persistent HTTP (HTTP1.1):
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT* for all the referenced objects (cutting response time in half)
  * Note that it still requires one RTT to establish connection for the first referenced object.

## Slide 11: HTTP - Improvement
HTTP/2
HTTP1.1: introduced multiple, pipelined GETs over single TCP connection
server responds in-order (FCFS: first-come-first-served scheduling) to GET requests
with FCFS, small object may have to wait for transmission (head-of-line (HOL) blocking) behind large object(s)
HTTP/2: [RFC 7540, 2015] increased flexibility at server in sending objects to client:
methods, status codes, most header fields unchanged from HTTP 1.1
transmission order of requested objects based on client-specified object priority (not necessarily FCFS)
divide objects into frames, schedule frames to mitigate HOL blocking

## Slide 12: HTTP - Improvement
HTTP 1.1: client requests 1 large object (e.g., video file) and 3 smaller objects
client
server
GET O1
GET O2
GET O3
GET O4
O1
O2
O3
O4
object data requested
O1
O2
O3
O4
objects delivered in order requested: O2, O3, O4 wait behind O1

## Slide 13: HTTP - Improvement
HTTP/2: objects divided into frames, frame transmission interleaved
client
server
GET O1
GET O2
GET O3
GET O4
O2
O4
object data requested
O1
O2
O3
O4
O2, O3, O4 delivered quickly, O1 slightly delayed
O3
O1

## Slide 14: HTTP - Improvement
Maintaining user/server state: cookies
Web sites and client browser use cookies to maintain some state between transactions
Example:
Susan uses browser on laptop, visits specific e-commerce site for first time
when initial HTTP requests arrives at site, site creates:
  unique ID (aka “cookie”)
  entry in backend database for ID
subsequent HTTP requests from Susan to this site will contain cookie ID value, allowing site to “identify” Susan

## Slide 15: HTTP - Improvement
Maintaining user/server state: cookies
client
Amazon server
usual HTTP response msg
usual HTTP response msg
cookie file
one week later:
usual HTTP request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
usual HTTP request msg
Amazon server
creates ID
1678 for user
create
entry
usual HTTP response
set-cookie: 1678
ebay 8734
amazon 1678
usual HTTP request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
amazon 1678
backend
database
time
time

## Slide 16: HTTP - Improvement
HTTP cookies: comments
What cookies can be used for:
authorization
shopping carts
recommendations
user session state (Web e-mail)
cookies and privacy:
cookies permit sites to learn a lot about you on their site.
third party persistent cookies (tracking cookies) allow common identity (cookie value) to be tracked across multiple web sites
aside
Privacy: Tracking a user’s browsing behavior
Challenge: How to keep state?

## Slide 17: Web Caches
Web caches (aka proxy servers)
user configures browser to point to a (local) Web cache
browser sends all HTTP requests to cache
  if object in cache: cache returns object to client
  else cache requests object from origin server, caches received object, then returns object to client
Goal: satisfy client requests without involving origin server
client
Web
cache
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
HTTP response
HTTP response

## Slide 18: Web Caches
Web caches (aka proxy servers)
Web cache acts as both client and server
  server for original requesting client
  client to origin server
Browser caching - Conditional GET: keep info up-to-date
  client: specify date of browser-cached copy in HTTP request
  server: response contains no object if browser-cached copy is up-to-date
Benefits:
  reduce response time for client request
  reduce traffic on an institution’s access link
  enables “poor” content providers to more effectively deliver content

## Slide 19: Caching example
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
Performance:
access link utilization = .97
LAN utilization: .0015
end-end delay = Internet delay +
access link delay + LAN delay
= 2 sec + minutes + usecs
Scenario:
access link rate: 1.54 Mbps
RTT from institutional router to server: 2 sec
web object size: 100K bits
average request rate from browsers to origin servers: 15/sec
  avg data rate to browsers: 1.50 Mbps
problem: large queueing delays at high utilization!
Notes: explain why minutes (recall earlier delay versus arrival rate curve from Chapter 1)

## Slide 20: Option 1: buy a faster access link
Performance:
access link utilization = .97
LAN utilization: .0015
end-end delay = Internet delay +
access link delay + LAN delay
= 2 sec + minutes + usecs
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
Scenario:
access link rate: 1.54 Mbps
RTT from institutional router to server: 2 sec
web object size: 100K bits
average request rate from browsers to origin servers: 15/sec
  avg data rate to browsers: 1.50 Mbps
154 Mbps
154 Mbps
.0097
msecs
Cost: faster access link (expensive!)
Notes: t’

## Slide 21: Option 2: install a web cache
Performance:
LAN utilization: .?
access link utilization = ?
average end-end delay = ?
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
Scenario:
access link rate: 1.54 Mbps
RTT from institutional router to server: 2 sec
web object size: 100K bits
average request rate from browsers to origin servers: 15/sec
  avg data rate to browsers: 1.50 Mbps
How to compute link
utilization, delay?
Cost: web cache (cheap!)
local web cache
Notes: t’

## Slide 22: Calculating access link utilization, end-end delay with cache:
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
local web cache
suppose cache hit rate is 0.4:
40% requests served by cache, with low (msec) delay
60% requests satisfied at origin
  rate to browsers over access link
  = 0.6 * 1.50 Mbps = .9 Mbps
  access link utilization = 0.9/1.54 = .58 means low (msec) queueing delay at access link
average end-end delay:
  = 0.6 * (delay from origin servers)
  + 0.4 * (delay when satisfied at cache)
  = 0.6 (2.0) + 0.4 (~msecs) = ~ 1.2 secs
lower average end-end delay than with 154 Mbps link (and cheaper too!)
Notes: t’

## Slide 23: Agenda
Web
  HTTP Protocol
  HTTP Improvement
  Web Caches
Email
  SMTP Protocol
FTP (Optional) discussion only*

## Slide 24: E-mail - Overview
Three major components:
user agents
mail servers
simple mail transfer protocol: SMTP
User Agent
a.k.a. “mail reader”
composing, editing, reading mail messages
e.g., Outlook, iPhone mail client
outgoing, incoming messages stored on server
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent

## Slide 25: E-mail - Overview
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent
mail servers:
mailbox contains incoming messages for user
message queue of outgoing (to be sent) mail messages
SMTP protocol between mail servers to send email messages
client: sending mail server
“server”: receiving mail server

## Slide 26: SMTP - Protocol
SMTP RFC (5321)
uses TCP to reliably transfer email message from client (mail server initiating connection) to server, port 25
  direct transfer: sending server (acting like client) to receiving server
three phases of transfer
  SMTP handshaking (greeting)
  SMTP transfer of messages
  SMTP closure
command/response interaction (like HTTP)
  commands: ASCII text
  response: status code and phrase
initiate TCP
connection
RTT
time
220
250 Hello
HELO
SMTP handshaking
TCP connection
initiated
“client”
SMTP server
“server”
SMTP server
SMTP transfers

## Slide 27: SMTP - Protocol
Mail message format
SMTP: protocol for exchanging e-mail messages, defined in RFC 5321 (like RFC 7231 defines HTTP)
RFC 2822 defines syntax for e-mail message itself (like HTML defines syntax for web documents)
header
body
blank
line
header lines, e.g.,
  To:
  From:
  Subject:
  these lines, within the body of the email message area different from SMTP MAIL FROM:, RCPT TO: commands!
Body: the “message” , ASCII characters only

## Slide 28: SMTP - Protocol
Sample SMTP interaction
S: 220 hamburger.edu
C: HELO crepes.fr
S: 250 Hello crepes.fr, pleased to meet you
C: MAIL FROM: <alice@crepes.fr>
S: 250 alice@crepes.fr... Sender ok
C: RCPT TO: <bob@hamburger.edu>
S: 250 bob@hamburger.edu ... Recipient ok
C: DATA
S: 354 Enter mail, end with "."
C: Do you like ketchup?
C: How about pickles?
C: .
S: 250 Message accepted for delivery
C: QUIT
S: 221 hamburger.edu closing connection
initiate TCP
connection
RTT
time
220
250 Hello
HELO
SMTP handshaking
TCP connection
initiated
“client”
SMTP server
“server”
SMTP server
SMTP transfers

## Slide 29: SMTP - Protocol
Scenario: Alice sends e-mail to Bob
1) Alice uses UA to compose e-mail message “to” bob@someschool.edu
4) SMTP client sends Alice’s message over the TCP connection
user
agent
mail
server
mail
server
1
2
3
4
5
6
Alice’s mail server
Bob’s mail server
user
agent
2) Alice’s UA sends message to her mail server using SMTP; message placed in message queue
3) client side of SMTP at mail server opens TCP connection with Bob’s mail server
5) Bob’s mail server places the message in Bob’s mailbox
6) Bob invokes his user agent to read message

## Slide 30: SMTP - Protocol
Retrieving email: mail access protocols
sender’s e-mail
server
SMTP
SMTP
receiver’s e-mail
server
e-mail access
protocol
(e.g., IMAP, HTTP)
user
agent
user
agent
SMTP: delivery/storage of e-mail messages to receiver’s server
mail access protocol: retrieval from server
  IMAP: Internet Mail Access Protocol [RFC 3501]: messages stored on server, IMAP provides retrieval, deletion, folders of stored messages on server
  POP3: Post Office Protocol—Version 3
HTTP: gmail, Hotmail, Yahoo!Mail, etc. provides web-based interface on top of STMP (to send), IMAP or POP or HTTP to retrieve e-mail messages

## Slide 31: SMTP: observations
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses CRLF.CRLF to determine end of message
comparison with HTTP:
HTTP: client pull (in most cases)
SMTP: client push
both have ASCII command/response interaction, status codes
HTTP: each object encapsulated in its own response message
SMTP: multiple objects sent in multipart message

## Slide 32
Thanks
Acknowledgment
The materials for this course are in part based upon the materials from a number of people/sources, including:
Official website of the Kurose and Ross text: Computer Networking: A Top-Down Approach
Official website of the Tanenbaum & Wetherall text: Computer Networks
Dr. Murat Yuksel: https://www.ece.ucf.edu/~yuksem/teaching/EEL-4781-Fall-2020.html
Dr. Raj Jain: https://www.cse.wustl.edu/~jain/

## Slide 33: Recap
Network Core
  Two key functions:
  Two ‘switching’ strategies:
  Packet-switching:
    store-and-?
    an important example
  Some terms: ISP, CPN
Protocols
  Five layers
  Encapsulation
  Security
    packet “sniffing”:
    IP spoofing: send packet with false source address
    Denial of Service (DoS)

## Slide 34: Recap
Network Core
  Two key functions: Forwarding and Routing
  Two ‘switching’ strategies: circuit-switching vs packet-switching
  Packet-switching:
    store-and-forward
    an important example
  Some terms: ISP, CPN
Protocols
  Five layers
  Encapsulation
  Security
    packet “sniffing”:
    IP spoofing: send packet with false source address
    Denial of Service (DoS)

## Slide 35: Recap
Application Layer
  Two paradigms:
  3 dimensions:
    Identifier:
    Interface of services:
    Protocol: HTTP, SMTP…
  Two services:
HTTP (HyperText Transfer Protocol)
  Paradigm:
  Service:
  Format
    Request:
    Response
  Features:
    Non-persistent vs Persistent: how many RTTs
    Stateless vs Stateful:
Transport Layer: 3-35

## Slide 36: Recap
Application Layer
  Two paradigms: server-client, peer-to-peer
  3 dimensions:
    Identifier: IP address and port number
    Interface of services: Socket
    Protocol: HTTP, SMTP…
  Two services: TCP, UDP
HTTP (HyperText Transfer Protocol)
  Paradigm: S-C
  Service: TCP
  Format
    Request: GET, HEAD, POST, PUT (pull or push?)
    Response
  Features:
    Non-persistent vs Persistent: how many RTTs
    Stateless vs Stateful: cookies
Transport Layer: 3-36